## Slide 1
FIXS · XIL BENCH · DESIGN STUDY
Axle Dyno ↔ CARLA
The dyno loop needs one signal from the vehicle model. CarMaker puts it on the wire. CARLA will not, and no configuration changes that — so the two designs here are two ways of routing around it.
I * dw/dt = Taxl + Trq_T2W
^^^^^^^ CARLA will not give you this
Design A impose the speed dyno owns longitudinal, CARLA is told the answer
Design B inject the torque CARLA's tire and body run, speed recovered from motion
Both are lumped single-axis. Per-wheel needs a fork.

## Slide 2
02 / 06 THE WALL — ON 0.9.15
What CARLA 0.9.15 will and will not tell you
The data exists and is computed every tick. On 0.9.15 there is no way to ask for it. On 0.9.16 there is — see slide 06.
READABLE
get_velocity get_transform
get_angular_velocity get_control
get_acceleration get_physics_control
get_wheel_steer_angle <- the only
per-wheel getter
NOT READABLE
wheel speed omega_i
longitudinal slip kappa_i
tire force Fx_i
normal load Fz_i
wheel torque Trq_T2W
but all of it is already computed and stored:
UVehicleWheel (UE4) DebugLongSlip DebugLatSlip DebugTireLoad
DebugWheelTorque DebugLongForce DebugLatForce
CARLA already holds the pointer: CarlaWheeledVehicle.cpp:309
show_debug_telemetry renders them to the HUD. There is no RPC path.
Consequence on 0.9.15: Trq_T2W and omega_i are both unavailable, and the two designs that follow are ways of living with that.

## Slide 3
03 / 06 DESIGN A
Impose the speed
The dyno owns all longitudinal dynamics, including road load from the vehicle's own measured coefficients. CARLA is told the answer.
DYNO + ROAD LOAD
Taxl from the real vehicle
A, B, C from real coastdown
-> v(k)
CARLA
enable_constant_velocity
( v, 0, 0 ) body frame
pose · lateral · traffic
HUB DYNOS
w_cmd_i = v / r
evenly to all units
longitudinal only
MEASURED
rejects any external force completely; the residual is exactly
one integration step of it and does not accumulate.
On a 20-degree slope the error was 0.069 m/s -- 0.46%.
the wheels keep up: tau = J_w*v/(r^2*Cs) = 3.4e-4 * v
10 m/s -> 3.4 ms 20 -> 6.8 ms 30 -> 10.2 ms
against a 20-50 ms tick, 3 to 15 time constants.
WHAT IT COSTS
writing along the nose imposes ZERO SIDESLIP
measured 0.45 deg, against 21 deg for a free car
in the same corner.
the car moves exactly where it points. Yaw is still
dynamic, so the path is right -- what you lose is
drift, oversteer, anything at the friction limit.
Use enable_constant_velocity, not set_target_velocity: the former is latched and in body frame (held 15.00 m/s indefinitely,
within 1.3 deg of the nose through a 130 deg turn). The latter is a one-shot world-frame write. Both need physics ENABLED.

## Slide 4
04 / 06 DESIGN B
Inject the torque
CARLA's own tire, wheel and body physics run. The bench feeds torque through the pedals; the wheel speed is recovered from the body's motion.
FIRST: the drivetrain has to be flattened, or throttle is not a torque
STOCK
moi = 1.0 through final_ratio = 9
= 81 kg m^2 at the wheel = 592 kg
plus clutch slip
MEASURED: 47% spread across throttle
FLATTENED (setup-time, once)
moi 0.01 · clutch 1e4 · final 1.0
one gear 1.0 · autobox off
flat torque curve · damping 0
MEASURED: 2.7% spread, 1.1% of predicted
Taxl >= 0 : throttle = Taxl / T0
Taxl < 0 : brake = |Taxl| / ( n_wheels * max_brake_torque )
THEN: recover the wheel speed from the body
sum Fx = m * dv/dt + Fres(v) + m*g*sin(theta)
Trq_T2W = -r * sum Fx
Fres is the ONLY chassis force besides gravity -- everything else is inside Fx
Difference get_velocity for dv/dt. Do NOT use get_acceleration -- it read 15.55 m/s^2 vertically on a stationary car.

## Slide 5
05 / 06 THE CEILING
Both designs are lumped, single-axis
Not by choice. The public API constrains it at both ends, so a per-wheel hub dyno gains nothing from Design B over Design A.
IN
throttle is ONE scalar. Torque reaches the
wheels through CARLA's differential, which
decides the split.
Left and right cannot be commanded apart.
OUT
the vdot inverse yields sum Fx from body
acceleration. Splitting it per wheel needs
per-wheel Fz and slip.
Neither is exposed.
THE ONLY PER-WHEEL PATH IS A FORK — and the engine class already exists
USimpleWheeledVehicleMovementComponent -> PxVehicleNoDrive
"a simple PxNoDrive which will give us suspension but no engine forces which we leave to the user"
void SetDriveTorque(float DriveTorque, int32 WheelIndex);
void SetBrakeTorque(float BrakeTorque, int32 WheelIndex);
void SetSteerAngle (float SteerAngle, int32 WheelIndex);
Per-wheel torque, no engine, suspension and tires intact. What is missing is a CARLA vehicle class that uses it -- CARLA already
has the pattern, since ACarlaWheeledVehicleNW sits alongside the 4W one -- plus the RPC bindings. A scope decision, not a technical one.

## Slide 6
06 / 06 0.9.16 CHANGES THE ANSWER
get_telemetry_data makes both signals readable
We are on 0.9.15.2. Everything on slides 02 and 04 exists to work around a signal that the next release exposes directly.
carla.WheelTelemetryData -- per wheel, read-only, no HUD needed
omega <- WHEEL SPEED tire_load <- Fz
torque <- Trq_T2W long_force <- Fx
long_slip <- kappa lat_force <- Fy
lat_slip <- alpha tire_friction, normalised forms
VehicleTelemetryData: speed steer throttle brake engine_rpm gear drag
WHAT IT RETIRES
the vdot inverse -- read torque directly
the unverified 2.52 m^2 drag area -- drag is reported
per-wheel READ needing a fork -- telemetry is per wheel
open items C-1, C-3, C-4, C-5
WHAT IT DOES NOT
telemetry is READ-ONLY. Injecting Taxl still goes
through apply_control -- one scalar throttle, split
by CARLA's differential.
So: measure per wheel, command lumped.
Per-wheel COMMAND still needs the SimpleWheeled fork.
Taxl_i -> pedal map -> CARLA -> get_telemetry_data().wheels[i].omega -> w_cmd_i
.wheels[i].torque -> Trq_T2W_i
That is the CarMaker loop, per wheel, with no reconstruction and no fork. Upgrading is the highest-value action in this study.