## Slide 1: Co-Simulation and Integration – Current Focus
Flexible Interface
Flexible Interface
Image courtesy of dSPACE
Image courtesy of CARLA
(Virtual Test Drive, 2017)

## Slide 2: Debate: Existing interface VS Fully customized interface
Existing interface is Eclipse MOSAIC.
It is pretty heavy and based on JAVA.
It is not originally designed for integration with real-time control system. The synchronization may need significant modifications [double check this]. e.g. SUMO should wait for command from ego vehicle/dSPACE.
We don’t have full control on the codes.
The performance is not fully tested.
It does not support VISSIM, CARLA, VTD, IPG, ASM. i.e. we need to develop interfaces following their architecture to integrate these tools. No well established API for this yet.
If we are clear about all the components we want to integrate, e.g. traffic, communication, control, virtual environment, sensors, XIL, and all the information flow, I believe we could come up with a solution.

## Slide 3
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
XIL
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Communication
Ego (k+1)
Traffic Cmd (k+1)
Manager
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
XIL
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Request
Cmd (k+1)
Traffic Received at (k)
event based
.config
CAV Controller can be a separate module (updates 0.1 seconds) or integrated with Vehicle (updates faster)
.config defines for each controller and communication, what’s the ROI of vehicles to extract
Basic Structure
With Communication
Manager
.config
1
2
3
4
5
6
1
2
2
3
4
5
6
TCP/IP

## Slide 4
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
XIL
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
(Traffic Cmd (k+1))
Ego (k+1)
Traffic Cmd (k+1)
Sensors
Environment Info
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
Ego (k+1)
Traffic Cmd (k+1)
CAV Controller
Virtual Environment/Vehicle
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
CAV Controller
Virtual Environment/Vehicle
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Ego (k+1)
With Sensors
HPC Potential
Manager
.config
Manager
.config

## Slide 5
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
XIL
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Communication
Ego (k+1)
Traffic Cmd (k+1)
Manager
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
XIL
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Traffic (k)
Ego Cmd (k+1)
Ego (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Request
Cmd (k+1)
Traffic Received at (k)
event based
.config
Basic Structure
With Communication
Manager
.config
1
2
3
4
5
6
1
2
2
3
4
5
6
CAV controller within vehicle, i.e. in Simulink

## Slide 6: Further notes
Define a way to define information we extracted from SUMO, depends on application ROI
  region of interest around a ego vehicle
  particular parts of a road, i.e. for centralized controller
  around traffic light
Can be based on subscription of SUMO data, essentially specify objID, domain,
Define message sets
  traffic, i.e. vehicle information
  signal lights, phase and timing, detectors
Need to assign unique id for different message sets
Potential components: traffic, control/application, virtual environment/vehicle, HIL, communication, sensor, signal controller. What else?
Design everything is SUMO, then adapt VISSIM message structure as SUMO.

## Slide 7: What’s included
Signal controller in the loop (SCIP) is within the scope. Basically, needs to define ROI, i.e. intersections, and message set of phase and timing and detectors.
Naturally, it supports multiple clients/vehicles, so has potential for larger scale
With this setup, CAV controller can be in different languages with appropriate: a) TCP/IP interface b) parser for messages.
Thus, possibly avoid the need to convert VISSIM COM to .dll.

## Slide 8
Manager
Traffic Simulator
CAV Controller
Virtual Environment/Vehicle
Traffic (k)
Ego (k)
Traffic (k)
Ego (k)
Ego Cmd (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Ego (k+1)
Traffic Cmd (k+1)
Traffic (k)
An alternative approach, directly send traffic to Vehicle.
-Traffic data can be updated more timely
-Might be challenging to extend to HPC application, since more connections to the Manager

## Slide 10
Traffic Simulator
or
dll
config.yaml
FIX_Core.exe
VISSIM Liaison
SUMO Liaison
Message
& Socket Handler
Application Layer
FIXS Liaison
CAV Controller
Ego CAV
FIXS Liaison
Driver
Speed Cmd.
Pedal & Brake Cmd.
Vehicle Dynamics Model
XIL
Preceding Vehicles Info.
Ego Command
Ego Actual
Real-Sim Interface
Vehicle Simulator
FIXS Liaison
3D Digital Twin

## Slide 11
CAV Control
XIL
Traffic Microsimulation
CAV Control
XIL
Traffic Microsimulation
Real-Sim Approach
Conventional Approach

## Slide 12
Traffic Simulator
Traffic Layer
Coord Merge
Comms
Ego
127.0.0.1
1337
YAML ApplicationSetup
YAML XilSetup
Embedded in source code
Server
Client
Server
Client
Server
Client
Server
Client
Traffic Simulator
Traffic Layer
Coord Merge
Comms
Ego
127.0.0.1
1337
YAML ApplicationSetup
YAML XilSetup
Embedded in source code
Switch Flag
Server
Client
Server
Client
Server
Client
Client
Server
RSU
OBU
Server
Client
192.168.0.54
50067
XX
XX

## Slide 13
Traffic Simulator
Simulate one step
CAV Application Client
Flexible Real-Sim Interface
Traffic Layer
Application Layer
Traffic States
Cmd
Hold last states
Interpolation
Idle
Simulate one step
Traffic States
Actual
Cmd
Hold last states
Traffic Simulator
Simulate one step
CAV Application Client
Flexible Real-Sim Interface
Traffic Layer
Application Layer
Traffic States
Cmd
Hold last states
Interpolation
Idle
Simulate one step
Traffic States
Actual
Cmd
Hold last states
Cmd

## Slide 14
VISSIM:
Receive cmd acceleration a(t)
Receive actual ego acceleration a(t)
FOR each vehicle:
Get actual v(t)
Set desired acceleration a(t)
Send v(t)
Receive cmd acceleration a(t+dt)
Receive actual ego acceleration a(t +dt)
FOR each vehicle:
Get actual v(t +dt)
Set desired acceleration a(t +dt)
Send v(t +dt)
Traffic Layer:
Receive v(t)
Send v(t)
WAIT
Receive Control v(t+dt), a(t+dt)
Send v(t+dt) to ego
Get actual ego a(t+dt)
Send cmd a(t+dt)
Send actual ego a(t+dt)
Control Layer
Receive v(t)
Get Control v(t+dt), a(t+dt)
Send cmd ego v(t+dt)
Recv actual ego a(t+dt)
Send actual ego a(t+dt), cmd a(t+dt)
Ego Model
Receive cmd ego v(t+dt)
Send actual ego a(t+dt)

## Slide 15
Type equation here.

## Slide 16
SUMO:
Send v(t)
Receive v(t+dt)
Simulate next step
Traffic Layer:
Receive v(t)
Send v(t)
WAIT
Receive v(t+dt)
Send v(t+dt)
Control Layer
Receive v(t)
Get Control v(t+dt), a(t)
Send cmd ego v(t+dt)
Recv actual ego v(t+dt)
Send actual ego v(t+dt), cmd traffic v(t+dt)
Ego Model
Receive cmd ego v(t+dt)
Send actual ego v(t+dt)
Traffic Simulator
CAV Application Client
Flexible Real-Sim Interface
Traffic Layer
Application Layer
Traffic States
Cmd
Hold last states
Interpolation
Idle
Simulate one step
Traffic States
Actual
Cmd
Hold last states

## Slide 17
Traffic Simulator
Flexible Real-Sim Interface
Traffic Layer
Application Layer
Application Layer
Application Layer
Signal Controller
Ego CAV 1
Vehicle Simulator
HIL Testbed
Ego CAV 2
Vehicle Simulator
HIL Testbed
(b) Distributed Architecture
CAV Application Clients
Vehicle All
Detector All
Tls All
Combined received data is on the Traffic Layer side
Traffic Layer distribute combined data to Application Layer and to two VISSIM dlls
VISSIM dlls need to know all Application Layer needs and send out message
Detector All
Tls All
Tls dll
drivermodel dll
Detector All
Tls All
Vehicle All
Vehicle[0]
Detector[0]
Tls[0]
Vehicle[1]
Detector[1]
Tls[1]
Vehicle[2]
Detector[2]
Tls[2]
Combined
Vehicle All
Detector All
Tls All
Combined
Vehicle All
Detector All
Tls All

## Slide 18
simState | simTime [float] |  |  |  | TotalMessageSize [uint32] |  | 
 | MessageSize |  | identifier | String size | f | l | o
w | _ | 0 | . | 0 |  |  | 
MessageSize |  | identifier | String size |  |  |  | 

## Slide 19
Simulation Time
(4 bytes)
Total Message Size
(4 bytes)
Data Length
(2 bytes)
Data Body
Data Length
(2 bytes)
Data Body
Header
Data Frame 1
Data Frame 2
Simulation State (1 byte)
Data ID (1 byte)
Data ID (1 byte)
String Length (1 byte)
String Body
Vehicle Data Body
String Length (1 byte)
String Signal Name
Signal Data Body
Signal ID
(2 bytes)
2 bytes (0-65535/-32768-32767)
ID
(1 bytes)
String Length (1 byte)
String Detector Name
State
(1 bytes)
ID
(1 bytes)
String Detector Name
State
(1 bytes)
String Length (1 byte)
String Length (1 byte)
String Signal Name
Signal ID
(2 bytes)
Detector Data Body
Data Length
(2 bytes)
Data ID (1 byte)
Signal Identifier
Detector 1
Detector 2
String Signal State
String Length (1 byte)

## Slide 20
id, speed, accelerationDesired, hasPrecedingVehicle, precedingVehicleDistance, precedingVehicleSpeed, signalLightDistance, signalLightColor, speedLimit, speedLimitNext, speedLimitChangeDistance
Little Endian, i.e., need to fliplr to get correct bit
Conversion:
The value of a IEEE-754 number is computed as:
sign 2exponent mantissa
The sign is stored in bit 32. The exponent can be computed from bits 24-31 by subtracting 127. The mantissa (also known as significand or fraction) is stored in bits 1-23. An invisible leading bit (i.e. it is not actually stored) with value 1.0 is placed in front, then bit 23 has a value of 1/2, bit 22 has value 1/4 etc. As a result, the mantissa has a value between 1.0 and 2. If the exponent reaches -127 (binary 00000000), the leading 1 is no longer used to enable gradual underflow.

## Slide 21: Current support vehicle data list
std::string id;
std::string type;
float speed;
float acceleration;
float positionX;
float positionY;
float positionZ;
float heading;
uint32_t color; // r,g,b,a
std::string linkId;
int32_t laneId;
float distanceTravel;
float speedDesired;
float accelerationDesired;
bool hasPrecedingVehicle;
std::string precedingVehicleId;
float precedingVehicleDistance; // distance to preceding vehicle
float precedingVehicleSpeed; // absolute speed of preceding vehicle
float signalLightDistance; // distance to next signal light
int8_t signalLightColor; // color of next signal light
float speedLimit;
float speedLimitNext;
float speedLimitChangeDistance;
std::string linkIdNext;
float grade; // angle in radians, positive climbing up hill
[id, type, speed, acceleration, positionX, positionY, positionZ, heading, color, linkId, laneId, distanceTravel, speedDesired, accelerationDesired, hasPrecedingVehicle, precedingVehicleId, precedingVehicleDistance, precedingVehicleSpeed, signalLightDistance, signalLightColor, speedLimit, speedLimitNext, speedLimitChangeDistance, linkIdNext, grade]

## Slide 22
If no preceding vehicle, should ignore the id, distance, speed,
If no signal, signallight distance will be negative
If no speed limit, speed limit will be negative

## Slide 23
Color rgba
first 8 bits r
second 8 bits g

## Slide 24
traffic signal data
string id
phase
detector list
detector vehicle

## Slide 25
Sensor data

## Slide 32
At (k) (traci.simulation.getTime()), getSpeed return speed at (k-1), getAcceleration return acceleration at (k-2), if using
setPreviousSpeed at (k) will change speed (k-1), then SUMO calculate acceleration (k-1), return speed (k) at (k+1)
setSpeed at (k) will change speed (k)
speed, acceleration from SUMO driver command
actual speed, acceleration (send to setPreviousSpeed)
Actual
Command

## Slide 33
0
0.1
0.1
0.2
0.2
0.3
0.3
Run one-step
Run one-step
Run one-step
Wait
Wait
Wait
0.1
0.2
0
placeholder, not used
SUMO
Simulink
Receive
Send
Send
Receive
Receive
Roundtrip delay
Roundtrip delay

## Slide 34
SUMO angle

## Slide 35
Vehicle will be gone after E3. so we only need getNextLinks once then can store the speed limit

## Slide 36
VISSIM does not have a typical speed limit information.
When there’s a reduced speed area, it will show the distance to that RSA.
When there’s desired speed decision, there’s no distance information until vehicle on the DSD
RSA change desired speed temporarily (only when within RSA). But vehicle will decelerate way ahead of RSA
DSD will permanently change desired speed, but vehicle will only change desired speed when passing DSD
To properly get a normal speed limit,
First need a python script to get a table of desired speed decision locations with regarding each link
a link can have multiple DSD
Then in dll, based on current link information and position, can find out what is next DSD
Then based on next link information, can find out the first DSD of the next link
Thus, we will have three data fields:
  float speedLimit;
  float speedLimitNext;
  float speedLimitChangeDistance;
Need to check if we force an ego vehicle, will next link information messed up

## Slide 37
If in VISSIM you define a 3D road, the speed position, etc. will still follow the 2D projected road
Next link only return when a vehicle enter the route decision regions
VISSIM will return each of the next links one by one for each vehicle
VISSIM combine static route, the two decisions have to be on the same link
// there will be next link only when the vehicle is in static decision areas
// the next links will contain all links within the static decision areas
// if used combine route, then will be able to see longer future routes
Speed limit connect to next has to guess
since do not know the link connection topology and route selection information
Next link information may not known
Initial speed limit may not known
Distance has to be distinct
Need to add UDA position on link, make sure no such no and name
Challenges:
Need both next link and lane, but may not have such information
Desired speed defined as a distribution
Desired speed decision defined for each class of vehicle
Desired speed decision define for each lane
No link topology (length, connection, lanes, etc.) information in dll. Need another lookup table
No initial speed limit

## Slide 38
Signal light, where do you want to get? Matlab or Simulink

## Slide 39
whether time of adding these CAV is known ahead of simulation or will be determined during the simulation? if latter, will simulink make the decision? what if want matlab to make the decision?

## Slide 40
Doing vehicle signal control, need extract information using dll.
Grade and 3D length, speed, position question
Speed limit how to properly obtain, since no route of a vehicle
Designate route when adding a vehicle, or change a route
Dll, position on network
Dll, add remove a vehicle
October PTV America's 23rd Annual User Group Meeting in Denver, CO!
Grade seems that still not right

## Slide 41
Mapping

## Slide 42
At (k) (traci.simulation.getTime()), getSpeed return speed at (k-1), getAcceleration return acceleration at (k-2), if using
setPreviousSpeed at (k) will change speed (k-1), then SUMO calculate acceleration (k-1), return speed (k) at (k+1)
setSpeed at (k) will change speed (k)
speed, acceleration computed by SUMO
speed, acceleration external control
Actual
SUMO computed
Integration step