## Slide 1
FIXS · XIL BENCH · dev_v0.9.0
Axle Dyno ↔ CarMaker Coupling
How the working implementation exchanges torque and speed with CarMaker across a single scalar per corner — where the one-step delay comes from, why the loop is stable, and what the architecture cannot tell you about itself.
w[k] = w[k-1] + (K*Ts / I) * ( Taxl[k] + Trq_T2W[k] )
K = 1 Ts = 0.001 s I = Wheel.<i>.I (CarMaker parameter)
hardware · measured · physical
CarMaker · computed
our Simulink bypass

## Slide 2
02 / 06 THE LOOP
What each part owns, and what crosses between them
Three parts, four signals, one equation. The wheel speed is computed in Simulink and sent to both sides. Nothing else crosses.
HARDWARE
real powertrain on the dyno
The dyno speed controller
makes the shaft follow w.
SIMULINK — OUR BLOCK
w[k] = w[k-1]
+ (Ts / I) * ( Taxl[k]
+ Trq_T2W[k] )
Ts = 0.001 s, same step as CarMaker
I = Wheel.<i>.I, read from CarMaker
CARMAKER
tire, body, suspension, road
Uses w to find tire slip,
then returns the tire torque.
Taxl[k]
measured axle
torque [Nm]
w[k] as speed
command [rad/s]
w[k]
written to rotv
[rad/s]
Trq_T2W[k]
tire torque [Nm]
The same w[k] goes to both sides. CarMaker is given the computed speed, not the measured one.
The real shaft speed stays in the dyno controller. If the servo lags, CarMaker never finds out.
CarMaker has no wheel speed of its own. Its integrator went with the PowerTrain module, so ours is the only one.
CarMaker never uses Taxl either. We send it, but with the support torques zeroed nothing reads it.
Read it as a sentence: add the measured axle torque to the tire torque from CarMaker, divide by the wheel inertia, integrate.
CarMaker does this same integration natively in its DriveLine (RefMan Fig. 16.83). We rebuilt that block with the same inertia parameter,
matching IPG's own UserPowerTrain.mdl. All CarMaker brake torque is zeroed here, because real braking is already inside Taxl.

## Slide 3
03 / 06 WHEN
One integration step, in a fixed order
Everything from here on answers one question: how is Trq_T2W[k] produced. Start with when CarMaker computes it.
ONE INTEGRATION STEP
Ts = 1 ms
Vehicle
Steering
Suspension kinematics & compliance
Aerodynamics
Suspension forces
Tire
reads the wheel speed as it stands
Brake
PowerTrain <- our block
advances the wheel speed state
Body Frame advances the chassis states
uses w[k-1]
emits Trq_T2W[k]
w[k] = w[k-1] + (Ts / I) *
( Taxl[k] + Trq_T2W[k] )
The tire is evaluated before the wheel speed is advanced, so it uses the value the state holds at the start of the step.
That is what advancing an ODE state means. It is not a delay added by our bypass: CarMaker's own powertrain does the same thing.
Two states advance here
Wheel speed at the PowerTrain slot,
chassis afterwards at Body Frame.
Backward Euler
CarMaker's own solver; ours matches.
Single stage, so this runs once per step.
Do not add another step
A Memory block or rate transition on
Trq_T2W -> integrator -> rotv costs damping.

## Slide 4
04 / 06 HOW
What the tire model does with the wheel speed
The bench supplies one quantity: the wheel rotational speed. Follow it down through the tire model to the torque that comes back.
FROM THE BENCH
w[k-1] -> Rim_rotv
the wheel rotational speed, and nothing else
FROM CARMAKER'S BODY MODEL
P_v0_W · Fz · camber · muRoad
contact-point velocity, load, friction
1 SLIP longitudinal s = ( w · rBelt_eff - vx ) / |…| <- the bench sets this
lateral alpha = atan( vy / |vx| ) <- steering and body yaw
Both come from one contact-point velocity vector, split into its two components.
2 RELAXATION tau = sigma / vx sigma ~ 0.05 m the tire's only ODE states
The carcass takes a rolling distance to build force, so slip is low-passed before it becomes force. Everything else here is algebraic.
3 FORCES Fx = Gx(alpha) · Fx0(s) longitudinal force, reduced by cornering
Fy = Gy(s) · Fy0(alpha) lateral force, reduced by driving or braking
Gx and Gy are the friction ellipse: one contact patch, one friction budget, so the two directions take from each other.
4 SPIN-AXIS TORQUE Trq_T2W = -r · Fx + rolling resistance -> back to our integrator

## Slide 5
05 / 06 WHAT CAN GO WRONG
The wheel can oscillate against the tire
The wheel has inertia. The tire sits between it and the road and acts like a spring. That is an oscillator, and it exists on any real vehicle.
WHAT OSCILLATES
I
wheel rocks back
and forth
tire carcass
acts as a spring
road
The carcass has to flex before it can pass
force to the road. CarMaker gives that flex a
length: about 5 cm of rolling. A compliance is
a spring, and a spring against the wheel
inertia is an oscillator.
WHERE THE DAMPING COMES FROM
As the tire rolls it continuously lays down fresh rubber and renews its grip.
That is what settles the oscillation.
Faster rolling renews it faster, so damping grows with speed.
At a standstill there is none at all.
WHAT THE INTEGRATION STEP COSTS
The tire is evaluated once per step, from the wheel speed as it stood at
the start of it. That always removes a small, fixed amount of damping.
At road speed there is plenty to spare. Down near walking pace there is
not, and the trace can ring.
EXAMPLE — rotv OR Trq_T2W DURING A SLOW CRAWL
healthy
ringing
This oscillation is physical, not a modelling artefact. A real car has it: it is the same mechanism behind brake judder and ABS chatter.
Why we do not see it
Below 2 m/s CarMaker switches to its
stand-still tire model, and we put the dyno
in torque mode while stopping.
What raises the risk
A longer sample time, a smaller wheel
inertia, a shorter relaxation length,
or a second delay in the loop.
The frequency, if you want it
Tens of hertz for a passenger wheel; we
estimate 40-50 Hz from a textbook slip
stiffness. Read Cs from the tire file.

## Slide 6
06 / 06 SUMMARY
What we can rely on, and what to check
The loop is sound. Three reasons, then the two things it cannot report on itself, then the open items.
There is only one wheel speed
Not one in the model and another on the bench.
Ours is the only one, so the two cannot
disagree.
It is IPG's own bypass
Backward Euler at 1 ms, wheel inertia read
from CarMaker, block for block the same as
UserPowerTrain.mdl.
Errors stay small
A 2 N·m torque bias settles at about
0.24 m/s of speed offset. It does not grow:
slip stiffness and drag both push back.
We cannot see the servo error
CarMaker is given the commanded speed, so it never learns whether the shaft reached
it. If the servo saturates we integrate a torque produced at a different speed, and
nothing warns us. Log w_act - w_cmd and set an alarm on it.
We cannot check Taxl against the model
CarMaker never reads the axle torque, so a measurement error shows up only as that
small speed offset, which looks like any other modelling choice. Torque calibration
has to be done on the bench.
To check
Model.USE_MODE in the tire file. 13, 14 or 15
is expected. It decides both the lateral
coupling and the low-speed behaviour.
Recorded simplifications
All CarMaker brake torque zeroed, since real
braking is inside Taxl. Support torques
zeroed too: no squat, no mount reaction.
Full detail
doc/xil/AxleDynoCarMakerCoupling.md has the
step-indexed equations, the source
references and the open-item list.